## Slide 1
CPS 510
Virtual Memory: A Lightning Tour
Now with x86-64
Jeff Chase
Duke University

## Slide 2: OS: classical view
data
data
Programs run as
independent processes.
Protected system calls
...and upcalls (e.g., signals)
Protected OS kernel mediates access to shared resources.
Threads enter the kernel for OS services.
Each process has a private virtual address space and one or more threads.
The kernel code and data are protected from untrusted processes.

## Slide 3: Process VM/VAS (32-bit example)
0x0
0x7fffffff
Static data
Dynamic data
(heap/BSS)
Text
(code)
Stack
Reserved
The program uses virtual memory through its process’ Virtual Address Space:
An addressable array of bytes…
Containing every instruction it can execute…
And every piece of data those instructions can reference…
  E.g., read/write == load/store on memory
Partitioned into logical segments (regions, areas) with distinct purpose and use.
Every reference by a running program is interpreted in the context of its VAS.
  Resolves to a location in machine memory
N
high

## Slide 4: Linux x86-64 VAS layout
Program
idata
heap
stack
text
0x400000
0x600000
data
0x601000
r-x
r--
rw-
0x1299000
0x7fff1373b000
lib
lib
r-x
r-x
0x2ba976c30000
64K
0x7fff1375c000
libc.so
shared
library
rw- [anon]
rw- [anon]
N
high addresses
Example: the details aren’t important.
PIC

## Slide 5: Why per-process address spaces?
Goal: multiple processes in memory at once, safely.
  Uniform view of private memorysimple linking.
  Avoids dynamic relocation at launch (linker-loader)
Safe (isolation)…but not really necessary for that.
Option 1: per-process base+bounds registers
Option 2: segmentation w/ per-segment base+bounds.
Problem: these require variable partitioning memory allocation. Like a heap! Messy! (parking lot)
Paged VM avoids that with uniform memory allocation in fixed-size chunks (pages).
Also permits lazy demand-fetching and caching.

## Slide 6: Block maps
map
Large storage objects (e.g., files, segments) may be mapped so they don’t have to be stored contiguously.
Idea: use a level of indirection through a map to assemble a storage object from “scraps” in different locations.
The “scraps” can be fixed-size slots: that makes allocation easy because the slots are interchangeable (fixed partitioning). Fixed-size chunks of data or storage are called blocks or pages.
Example: page tables that represent a VAS.
One issue now is that each access must indirect through the map…
object

## Slide 7: Indirection

## Slide 8: Terminology: mapping
map, table,
index (inode)
Logical storage object
File
Segment
VAS
Volume
Logical block i
Virtual page i
Underlying storage space
Larger or smaller
Physical?
May itself be logical/virtual
Allocate slots from it
Slots: blocks, pages, frames
Virtual Page Number i
Page Frame Number j
Block or page may refer to either space.

## Slide 9: Virtual addressing
virtual
memory
(big?)
machine
memory
(small?)
Code running on a core addresses memory through virtual addresses.
The machine translates virtual addresses via an in-memory page table.
The OS controls the contents of the page table.
The machine allows a user process to access memory only by a valid translation in the page table.
Machine’s memory management unit (MMU) translates VAs through the map.
The page table represents a functional mapping of virtual pages (VPNs) to page frames (PFNs) for resident pages. If a page is not resident in memory, then its page table entry (PTE) is marked.

## Slide 10: Example: load from VA
MMU
Physical
address
(PA)
...
0:
1:
M-1:
Main memory
Virtual
address
(VA)
CPU
2:
3:
4:
5:
6:
7:
4100
Data word
4
CPU chip
Address
translation
[from CS:APP3e F9.2]
movl -32(%rbp), %rcx

## Slide 11: Virtual address translation
VPN
offset
12
Example: a typical 32-bit architecture with 4KB pages.
address
translation
Virtual address translation maps a virtual page number (VPN) to a page frame number (PFN/PPN) in machine memory: the rest is easy.
PFN
offset
+
0
machine address
(e.g., physical address)
{
Deliver fault to
OS if translation is not
valid and accessible in
requested mode.
virtual address
{

## Slide 12: Cartoon view of a page table
PFN x
PFN y
PFN z
VPN #i
offset
virtual address
PFN z
process page table (map)
machine memory
page frames
This is an example. Any PFN may be used for any VPN.
The map itself is just another data structure stored in memory.
A protected CPU register (CR3) holds the machine address of current map.
Virtual page: a logical block in a segment.
VPN: Virtual Page Number (a logical block number).
Page frame: a physical block in machine memory.
PFN: Page Frame Number (a block pointer).
PTE: Page Table Entry (an entry in the block map).
VPN = VA DIV PAGE_SIZE
Offset = VA MOD PAGE_SIZE

## Slide 13: Page tables/maps: some issues
That 64-bit VAS is huge! The maps must be huge too!
That VAS is sparse! (It has big holes.) So how much of the maps is just wasted storing null PTEs?
What about the cost of map lookup(s)? Doesn’t VM multiply the cost of accessing memory?
How to change VAS on a process switch?
What about restricted memory access modes? Disabling writes or execute?
What about demand fetch/fill? What if we reference a missing (not present/valid/resident) page?

## Slide 14
virtual address
32 bits
[from Tanenbaum]
Two-level page table
32-bit virtual address, 32-bit PTEs
Two 10-bit page table index fields (PT1, PT2)
(10 bits represents index values 0-1023)
Step 1. Index PDIR with PT1
Step 2. Index second-level page table with PT2
Example: Windows/IA32
(1 page)
Each “table” is 1 page.

## Slide 15: Example: Windows/IA32
Two-level block map (page table) structure reduces the space overhead for block maps in sparse virtual address spaces.
  Many process address spaces are small: e.g., a page or two of text, a page or two of stack, a page or two of heap.
This is a simple example of a hierarchical page table:
  Each VAS has a page directory (“PDIR”)
  The PDIR is one page: 4K bytes, 1024 4-byte entries (PTEs)
  Each PDIR entry points to a map page, which MS calls a “page table”
  Each map page (“page table”) is one page with 1024 4-byte PTEs
  Each PTE maps one 4K virtual page of the address space
  Therefore each map page (page table) maps 4MB of VM: 1024*4K
  Therefore one PDIR maps a 4GB address space, max 4MB of tables

## Slide 16: But where is the PDIR?
Each process has its own VAS, i.e., its own VM.
Therefore each process has its own page tables.
Therefore each process has its own PDIR etc.
How does the MMU “know” which process is running?
How does the MMU “know” where to find the PDIR?
  Answer: ???
On a page fault, how does the OS “know” the address?
  Answer: ???

## Slide 17: But where is the PDIR?
Each process has its own VAS, i.e., its own VM.
Therefore each process has its own page tables.
Therefore each process has its own PDIR etc.
How does the MMU “know” which process is running?
How does the MMU “know” where to find the PDIR?
  Answer: the OS tells it (e.g., in control register CR3).
On a page fault, how does the OS “know” the address?
  Answer: the machine tells it.
They pass this info through designated control registers.

## Slide 18: A real PTE: x86-64 (Intel Core i7)
PFN / PPN (40-bit)
G
0
D
A
CD
WT
U/S
R/W
P=1
51
12
8
7
6
5
4
3
2
1
0
Available for OS (e.g., page location on disk)
P=0
XD
63
[from CS:APP3e F9.24: edited and not to scale]
P: present bit: ”valid”? or “missing”? Set by OS software.
Protection bits
XD: execute disable: 1 -> no instruction fetch from this page
R/W: read-write privilege? or read-only?
U/S: accessible from user code? Or only by OS (supervisor)?
Status bits set by hardware, cleared by OS software
A: reference bit: 1-> page accessed since A last cleared by OS.
D: dirty bit: 1-> page written since D last cleared by OS.

## Slide 19: X86-64 (i7) 4-level maps
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
9
/
9
/
9
/
9
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry
[from CS:APP3e F9.25]

## Slide 20: Page walk and the TLB
Is it slow? Maybe.
But the MMU caches PTEs in its Translation Lookaside Buffer (TLB).
Hit rates are high.
VA
Processor
Trans-
lation
Cache/
memory
PA
Data
CPU chip
TLB
VPN
PTE
1
2
3
4
5
[from CS:APP3e]

## Slide 21: Memory as a cache: valid/present bits
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Backing store
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
[from CS:APP3e F9.4]
What if CPU addresses a “missing” VP?

## Slide 22: Missing page: page fault
null
null
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
Virtual address
VP 3
[from CS:APP3e F9.6]
VP 3 is missing: MMU triggers a page fault.
page table
VPN 3

## Slide 23: VM control registers (IA32)
See [en.wikipedia.org/wiki/Control_register]
The details aren’t important.
Protected mode Enable
Points to page table (in machine memory) for current VAS active on this core
Faulting VA (if page fault is active)
CR3

## Slide 24: After the fault
null
null
page table
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
Virtual address
VP 3
[from CS:APP3e F9.7]
Example: select VP 4 as the victim, reassign its frame to hold VP 3, load VP 3 from disk, and restart the faulting instruction.

## Slide 25: Virtual Addressing: Under the Hood
raise
exception
probe
page table
load
TLB
probe
TLB
access
physical
memory
access
OK?
page
fault?
kill
(lookup and/or)
allocate
frame
page on
“disk”?
fetch
from disk
zero-fill
load
TLB
start
here
MMU
OS
illegal reference
legal reference
yes
no (first reference)
yes
no
miss
hit
How to monitor page reference events/frequency along the fast path?
restart